## Slide 1: It’s like riding
Your Own ITDP PowerPoint Template
Better cities through better streets
Notes: Hello everyone, I am Aswathy Dilip. Welcome to today’s webinar on Creating better cities through better streets.

## Slide 2
Creating better streets
in Indian cities:
The journey
Better cities through better streets
Notes: Over the next hour, I will take you through ITDP India’s journey inspiring Indian cities to create better streets;

## Slide 3
Notes: 2009: Chennai’s vehicle population is rising at an alarming pace. We have 30.25 lakh registered vehicles in the city. We need more space for them!

## Slide 4
“I walk with my heart in my hand.”

## Slide 5
“I have been cycling for more than 40 years.”

## Slide 6
Two third of all trips are by walk, cycle or public
transport

## Slide 7
How world’s best cities are designed
How most cities are designed
Yet, the design of our streets tends to push the vulnerable users to the fringes of the road

## Slide 8: 3507
Resulting in loss of precious lives every day
pedestrians killed in Tamil Nadu in 2017.
Other states:
1831-Maharashtra
1379-Andhra Pradesh

## Slide 9
8/10 trips by women are on foot or public transport

## Slide 10
Designing ‘Complete Streets’ for all users and uses

## Slide 11
Inspiring champions and building
partnerships
A

## Slide 12
Pilots in collaboration with local designers

## Slide 13
Embed changes through standards and
policy adoption
B

## Slide 14
From 100kms to city-wide network plan

## Slide 15
Expanding transformation: Institutional
reforms and capacity building
C

## Slide 16
National Smart City Mission — a catalyst
Notes: 2015

## Slide 17
Developing national best practice standards

## Slide 18
Better cities through better streets
Complete Streets:
Policy Framework

## Slide 19
A street provides
Access to jobs, education and amenities
Economic Opportunities
An identity to a city
Social and Recreational Opportunities

## Slide 20
A street has many uses
Walking and Cycling
Formal & Informal Public Transport
Personal Motor Vehicles – mobile and parked: Utilities
For mobility & service infrastructure
Vending & Shopping : Eyes on the street
Gathering
Also as a public space

## Slide 21
A street hosts many people
Pedestrians and Cyclists
Women as much as men
Of different transport modes and gender, Different age groups and physicalities
The differently abled
Dependent and independent children and elderly

## Slide 22
Designing ‘Complete Streets’ for all users and uses

## Slide 23: PRINCIPLES 1. Efficient Mobility Multiple modes of travel High quality facilities for public and non-motorised transport Allocating space equitably for all users
Principles of Complete Streets

## Slide 24: PRINCIPLES 2. Safety Safe for all user groups Segregated spaces for each Traffic calming measures Personal safety good lighting Active edges and vending
Principles of Complete Streets

## Slide 25: PRINCIPLES 3. Universal Accessibility Accessible by all Continuous and even-surfaced footpaths Table top crossings and ramps Tactile pavers wherever level differences occur
Principles of Complete Streets

## Slide 26: PRINCIPLES 4. Liveability Full of life - elements that improve activity attracts more users Increases retail activity for all users - transforms the street into a vital public space
Principles of Complete Streets

## Slide 27: PRINCIPLES 5. Sensitivity to Local Context Designed to suit the local context Factoring in local street activities Patterns of pedestrian movement Nearby land uses and the needs of the people
Principles of Complete Streets

## Slide 28: PRINCIPLES 6. Environmental Sustainability Promotes sustainable modes of transport Improves local climatic conditions Reducing pollution and heat Capture and channel rainwater through design
Principles of Complete Streets

## Slide 29: Improves Sustainable Mode Share Case: St .Mark's road, Bangalore With the revamped design, pedestrian volumes have gone up by 250%
BEFORE
AFTER
Benefits of Complete Streets

## Slide 30: Improves Vibrancy Case: Strøget, Copenhagen The revamp led to 6 times more area for pedestrians and buses with 145 people/min
BEFORE
AFTER
Benefits of Complete Streets

## Slide 31: Reduces Fatalities Case: Plaza program, New York City The plaza program help reduce pedestrian accidents by 35%
BEFORE
AFTER
Benefits of Complete Streets

## Slide 32: Allows Equitable Mobility for all Case: Avenida 9 de Julio, Buenos Aires The revamped street reduced bus travel time by 63%
BEFORE
AFTER
Benefits of Complete Streets
Notes: positively impacting the lives of over 200,000 commuters

## Slide 33
Better cities through better streets
Complete Streets:
Policy Workbook

## Slide 34
Complete Streets Policy Process
01 Creation of Complete Streets Policy
02 Institutional Framework

## Slide 35: Invite all stakeholders — representatives from all road owning agencies, ULB, development authority, civil bodies, academia etc.   Present the draft vision and goals and build consensus
Creating a shared vision with all stakeholders
Notes: positively impacting the lives of over 200,000 commuters

## Slide 36: “What kind of city do we want to live in?” “How will mobility – in particular walking and cycling - in the cities in the future differ from what it is today?”
Creating a shared vision with all stakeholders
Notes: positively impacting the lives of over 200,000 commuters

## Slide 37: To improve coordination between various agencies at the city level To ensure consistent engagement with all stakeholders
Institutional Framework: Apex committee
Notes: positively impacting the lives of over 200,000 commuters

## Slide 38: To support planning, designing of streets. To oversee and monitor the work produced by design consultants, contractors as well as general maintenance of streets.
Institutional Framework: Complete Streets Cell
Notes: positively impacting the lives of over 200,000 commuters

## Slide 39
Better cities through better streets
Complete Streets:
Planning Workbook

## Slide 40
Creating continuous networks, not discontinuous segments
Completed in Phase 1
Ongoing street design packages

## Slide 41
Complete Streets Planning Process

## Slide 42
NMT Master plan
+
Pedestrian Network
Greenways Network
Cycle Network
+
Once the pedestrian, greenways and cycle networks are prepared, they should then be superimposed to create the NMT master plan.
PLANNING METHODOLOGY
Creating complete streets masterplan
Streets with segregated footpaths
Pedestrian only streets
Only NMT - PT streets
NMT Priority Streets
15/30 kmph zones around schools
Network of canals, lakes and other natural features
Streets with segregated cycle tracks
Cycle priority routes

## Slide 43
NMT Master plan
PLANNING METHODOLOGY
Determining the budget and phasing
Project Packaging
Design Recommendations
Project
Costing & Timeline
+
+
Based on the RoW and land use of each street, design recommendations for each street is provided.
Minimum 15-25 km depending on the total street network
Arterial street - the entire length be given to one consultant to ensure design continuity
Based on the type of project and the total length of the street, costs are calculated.

## Slide 44
Better cities through better streets
Complete Streets:
Design Workbook

## Slide 45
Complete Streets Design

## Slide 46
Complete Streets Design

## Slide 47
Design Process

## Slide 48
Street Design Elements

## Slide 49
FOOTPATH

## Slide 50
FOOTPATH
zones

## Slide 51
zones
Multi-utility zone
Pedestrian zone
Frontage zone
FOOTPATH

## Slide 52: Design templates Intersection templates Transit systems and the street Street materials Participatory street design
Street design templates
24M RoW
18M RoW
12M RoW
Notes: positively impacting the lives of over 200,000 commuters

## Slide 53
Better cities through better streets
Complete Streets:
Implementation Workbook

## Slide 54
Implementation process

## Slide 55
01 Pre construction Process
02 Construction Process
03 Post -Construction Process
Implementation process

## Slide 59
Better cities through better streets
Complete Streets:
Evaluation Metrics

## Slide 60
Complete Streets: Key indicators
Efficient Mobility | 
1 | Mode Share
2 | Registered vehicles data
3 | Daily Bus Ridership
Liveable, accessible and comfortable streets | 
4 | Share of mixed use along streets
5 | Active street segments
6 | Non-walking activities along the street
Safety | 
7 | Traffic injuries
8 | Traffic fatalities
Environmental Sustainability | 
9 | Annual mean particulate matter concentration at street level
Outcome Indicators:
1 | Extend of footpath ⬤ ⬤ ⬤ ⬤
2 | Share of footpath with adequate lighting ⬤ ⬤ ⬤ ⬤
3 | Extent of cycle track ⬤ ⬤ ⬤ ⬤
4 | Share of cycle track with adequate lighting ⬤ ⬤ ⬤ ⬤
5 | Share of paid parking under demand-pegged IT management system ⬤
6 | Ratio of parking revenue to property rent ⬤
7 | Operating buses per lakh population ⬤ ⬤ ⬤
8 | Ratio of monthly public transport travelling cost to EWS income ⬤ ⬤ ⬤
9 | Percentage of transport budget allocated for Complete Streets projects ⬤ ⬤ ⬤ ⬤
10 | No. of air quality monitoring stations at street level ⬤ ⬤ ⬤ ⬤
Core Output Indicators:

## Slide 61: I. Efficient Mobility: Tracks behavioural change from usage of person motor vehicles to walking, cycling and usage of public transport as better sustainable transport infrastructure is provided.
Outcome indicators
INDICATOR | DATA SOURCE | FREQUENCY | LEVEL OF DIFFICULTY | BENCHMARK
1. Mode Share - disaggregated by: Walk, Cycle, Bus, Rail, Metro, IPT, personal two-wheelers and personal four-wheelers | Household Survey | Every 5 years | ⬤ | 20% or more increase in walking and cycling from baseline
2. Registered vehicles data for last (financial/ calendar) year and for the preceding decade | Regional Transport Office (RTO) | Every year | ⬤ | Relative percentage decrease from baseline.
3. Daily ridership of buses (disaggregated by age, gender and ability) | Primary survey | Every year | ⬤ | 20% or more increase in ridership from baseline by women, children (5-15 years), elderly (more than 60 years), and people with disabilities
Notes: positively impacting the lives of over 200,000 commuters

## Slide 62
Core Output indicators
INDICATOR | DATA SOURCE | FREQUENCY | LEVEL OF DIFFICULTY | BENCHMARK
1. Accessibility/ Safety Percentage of street length with Continuous Barrier-free walking zone width as per IRC:103-2012 Maximum footpath height of 150mm | Accessibility audit | Every year | ⬤ | 1: 75% to 100% 2. 50% to 74% 3. 25% to 49% 4. Less than 24 %
2. Personal Security: Percentage of footpath with adequate lighting of 30 lux | Accessibility Audit between 7 - 9 pm | Every year | ⬤ | 1: 75% to 100% 2. 50% to 74% 3. 25% to 49% 4. Less than 24 %
I. Extent of Walking Envionment
Measures the accessibility, and security of the walking environment.
Notes: positively impacting the lives of over 200,000 commuters

## Slide 63
Better cities through better streets
Complete Streets:
Best Practices

## Slide 64
TN MEGA STREETS PROGRAMME
Before | DP Road, Pune

## Slide 65
TN MEGA STREETS PROGRAMME
After | JM Road, Pune

## Slide 66
TN MEGA STREETS PROGRAMME
After | DP Road, Pune

## Slide 67
TN MEGA STREETS PROGRAMME
After| JM Road, Pune

## Slide 68
TN MEGA STREETS PROGRAMME
After | JM Road, Pune

## Slide 69
TN MEGA STREETS PROGRAMME
After | DP Road, Pune

## Slide 70
TN MEGA STREETS PROGRAMME
After | Harrington Road, Chennai

## Slide 71
TN MEGA STREETS PROGRAMME
Before | Harrington Road, Chennai

## Slide 72
TN MEGA STREETS PROGRAMME
After | Harrington Road, Chennai

## Slide 73
TN MEGA STREETS PROGRAMME
After | Harrington Road, Chennai

## Slide 74
TN MEGA STREETS PROGRAMME
Before | Police Commissioner Road, Chennai

## Slide 75
TN MEGA STREETS PROGRAMME
After | Police Commissioner Road, Chennai

## Slide 76
TN MEGA STREETS PROGRAMME
Before | Raman Street, Chennai

## Slide 77
After | Raman Street, Chennai

## Slide 78
TN MEGA STREETS PROGRAMME
Shared street | Church Street, Bangalore

## Slide 79
TN MEGA STREETS PROGRAMME
Pedestrian priority street | Ped plaza, Chennai

## Slide 80
TN MEGA STREETS PROGRAMME
Pedestrian street | SM Street, Kozhikode

## Slide 81
fb.com/itdpindia
india@itdp.org
india.itdp.org
twitter.com/itdpindia
Better cities through better streets
By Aswathy Dilip
aswathy.dilip@itdp.org
www.itdp.in